## Slide 1: Diffusion MRI Analysis
Sonia Pujol, Ph.D.
Surgical Planning Laboratory
Harvard University

## Slide 2: Brain Anatomy
White matter ~45% of the brain
Myelinated nerve fibers
(~ 10 μm axon diameter)

## Slide 3: White Matter Exploration
Jules Joseph Dejerine (Anatomie des centres nerveux (Paris, 1890-1901): Atlas of Neuroanatomy based on myelin stained preparation

## Slide 4: Diffusion Tensor Imaging (DTI)
First non-invasive window on white matter anatomy
Measurement of the motion of water molecules using MRI techniques.
Three-dimensional reconstruction of the trajectory of white matter bundles

## Slide 5: Diffusion Weighted Imaging (DWI)
S1
S2
S3
S0
S0
S6
S7
S8
S4
S5
S9
S10
S11
S12
In this example, the DWI scan was acquired with 12 diffusion sensitizing gradient directions (S1-S12) and 2 non-diffusion sensitizing gradients (S0)

## Slide 6: From DWI to DTI
Stejskal-Tanner (1965)
DWI
DTI
Si: DWI volume acquired with ith gradient
So: Baseline volume
S1
S2
S3
S0
S0
S6
S7
S8
S4
S5
S9
S10
S11
S12
DWI dataset acquired with 12 gradient and 2 baseline
DTI dataset

## Slide 7: Diffusion Tensor Imaging

## Slide 8: Diffusion Tensor Imaging
zz
zy
zx
yz
yy
yx
xz
xy
xx
D
D
D
D
D
D
D
D
D
D=

## Slide 9: Diffusion Tensor Imaging
zz
zy
zx
yz
yy
yx
xz
xy
xx
D
D
D
D
D
D
D
D
D
D=
λ1
λ2
λ3

## Slide 10: Tractography
DTI tractography provides 3D reconstruction of the trajectory of white matter pathways
Notes: Tractography us tract finding algorithm

## Slide 11: Tutorial Outline
This tutorial is an introduction to the fundamentals of Diffusion MRI analysis, from the estimation of diffusion tensors to the interactive 3D visualization of fiber tracts.

## Slide 12: Tutorial Dataset
The tutorial dataset DiffusionMRI_tutorialData is a Diffusion Weighted MR scan of the brain acquired with 41 gradient directions and one baseline.
Diffusion Sensitizing Gradients
Diffusion Weighted Images
Download the dataset at:
https://www.slicer.org/w/images/e/e6/Dti_tutorial_data.zip

## Slide 13: 3D Slicer
The tutorial uses the 3D Slicer (Version 4.10, Stable Release) software available at:
http://download.slicer.org
Disclaimer
It is the responsibility of the user of 3DSlicer to comply with both the terms of the license and with the applicable laws, regulations and rules. Slicer is a tool for research, and is not FDA approved.

## Slide 14: SlicerDMRI
An open-source project to improve and extend diffusion magnetic resonance imaging software in 3D Slicer:
http://dmri.slicer.org
Disclaimer
It is the responsibility of the user of 3DSlicer to comply with both the terms of the license and with the applicable laws, regulations and rules. Slicer is a tool for research, and is not FDA approved.

## Slide 15: Install SlicerDMRI
First, start Slicer

## Slide 16: Install SlicerDMRI
Click on the Diffusion menu; then, click on Install Slicer Diffusion Tools
Click on the Modules menu

## Slide 17: Install SlicerDMRI
Click Install SlicerDMRI

## Slide 18: Install SlicerDMRI
Click Yes to install UKFTractography

## Slide 19: Install SlicerDMRI
Click OK to restart Slicer and finish installation

## Slide 20: Install SlicerDMRI
Related modules appear in the Diffusion menu

## Slide 21: Learning Objectives
Following this tutorial, you’ll be able to
1) Estimate a tensor volume from a set of Diffusion Weighted Images
2) Understand the shape and size of the diffusion ellipsoid
3) Reconstruct DTI tracts from a pre-defined region of interest
4) Interactively visualize DTI tracts seeded from a fiducial

## Slide 22: MR Diffusion Analysis Pipeline
DWI Acquisition
Tensor Calculation
Scalar Maps
3D Visualization

## Slide 23: Part 1: From DWI images to Tensors

## Slide 24: Understanding the DWI Dataset
The Diffusion Weighted Imaging (DWI) dataset is composed of 41 volumes acquired with 41 different diffusion-sensitizing gradient directions, and one baseline image acquired without diffusion weighting.
….

## Slide 25: Loading the DWI Dataset
In your files archive, locate the file dwi.nrrd in the dataset folder for this tutorial
Drag and drop the file dwi.nrrd onto the viewer of the Slicer application

## Slide 26: Loading the DWI Dataset
Exit the archive folders window, and click OK to load the dataset to Slicer

## Slide 27: Loading the DWI Dataset
Slicer displays DWI volume of the brain

## Slide 28: Loading the DWI Dataset
Click on the Modules menu and select the module Volumes

## Slide 29: Loading the DWI Dataset
The baseline image corresponds to the DWI Component #0.
Select the DWI Component #10, which corresponds to the 10th diffusion sensitizing gradient

## Slide 30: Loading the DWI Dataset
For image contrast adjustment, you may use the Manual W/L slider.

## Slide 31: Loading the DWI Dataset
Position your mouse over the pin icon, then click on the link icon and the fit image to window icon

## Slide 32: Loading the DWI Dataset
Click on the Slicer layout menu and select the Red slice only layout

## Slide 33: Loading the DWI Dataset
Slicer displays only the Axial anatomical slice in the Viewer

## Slide 34: Creating a brain mask
Click on the Modules menu, then select Diffusion -> Process -> Diffusion Brain Masking

## Slide 35: Creating a brain mask
-select the Input DWI volume ‘dwi’
-select Output Baseline Volume ‘Create new Volume as...’, and name it ‘baseline’
-select Output Diffusion Brain Mask ‘Create new LabelMapVolume as...’, and name it ‘brain_mask’
-click on Apply.

## Slide 36: Creating a brain mask
Slicer displays the edited brain mask

## Slide 37: Creating a brain mask
Change the label layer to None to make the mask invisible

## Slide 38: Estimating the tensor
Click on the Modules menu, then select Diffusion -> Process -> Diffusion Tensor Estimation

## Slide 39: Estimating the tensor
-Set the Input DWI volume to ‘dwi’
-Set the Input Brain Mask to ‘brain_mask’
- Select Output DTI Volume ‘Create DiffusionTensorVolume as ...’, and name it ‘dti’
-Set Output Baseline Volume to ‘baseline’
-Under ‘Advanced Settings’, set Fitting Methods to ‘WLS’ (Weighted Least Squares)
-Click on Apply.

## Slide 40: Estimating the tensor
Position your mouse over the pin icon, click on the double arrow and select the dti in the B field, set the F and L to none.

## Slide 41: Exploring the DWI Dataset
Slicer displays the DTI volume in color by orientation mode:
Red: right-left
Green: anterior-posterior
Blue: inferior-superior

## Slide 42: Diffusion Tensor Data
zz
zy
zx
yz
yy
yx
xz
xy
xx
D
D
D
D
D
D
D
D
D
D=
Stejskal-Tanner equation (1965)
The diffusion tensor D in the voxel (I,J,K) is a 3x3 symmetric matrix.

## Slide 43: Diffusion Tensor
Scalar maps can be derived from the rotationally invariant eigenvalues λ1, λ2, λ3 to characterize the size and shape of the diffusion tensor.
λ1
λ2
λ3
The diffusion tensor D in each voxel can be visualized as a diffusion ellipsoid, with the eigenvectors indicating the directions of the principal axes, and the ellipsoidal proportional to the square root of the eigenvalues defining the

## Slide 44: Diffusion Tensor Shape
λ1>> λ2, λ3
λ1= λ2= λ3
λ1~λ2>> λ3
Anisotropic media
(white matter)
Isotropic media
(Cerebrospinal Fluid, gray matter)

## Slide 45: Exploring the DWI Dataset
Click on the Slicer layout menu and select the Yellow slice only layout.

## Slide 46: Corpus Callosum
The corpus callosum is a broad thick bundle of dense myelinated fibers that connect the left and right hemisphere. It is the largest white matter structure in the brain
Image from Gray’s Anatomy

## Slide 47: Corpus Callosum
Corpus Callosum

## Slide 48: Characterizing the Size of the tensor: Trace
Trace(D) = λ1+ λ2+λ3
Trace(D) is intrinsic to the tissue and is independent of fiber orientation, and diffusion sensitizing gradient directions
Trace(D) is a clinically relevant parameter for monitoring stroke and neurological condition (degree of structural coherence in tissue)
Trace(D) is useful to characterize the size of the diffusion ellipsoid

## Slide 49: Trace
Click on the Modules menu, then select Diffusion -> Quantify -> Diffusion Tensor Scalar Maps

## Slide 50: Trace
Type in the following information in the IO menu:
-select the Operation ‘Trace’
-set Input DTI Volume to ‘dti’
-select Output Volume ‘Create new Volume as...’ and name it ‘trace’
-click on Apply to calculate the trace map of the tensor volume

## Slide 51: Trace
The trace image appears in the yellow viewer
Set L as none.

## Slide 52: Trace
Adjust window level by right-dragging up and down.

## Slide 53: Trace
Position your mouse over the pin icon and then select the ‘>>’ icon to display this table and fill in the following information:
-Select the volume ‘trace’ in the Background viewer
-Select the volume ‘dti’ in the Foreground viewer
Set the opacity of the dti volume to 0.40

## Slide 54: Trace
Position your mouse within the region of the Corpus Callosum and observe the trace values in the Data Probe

## Slide 55: Trace
Note how the Trace values are fairly uniform in both white and gray matter, even if the tissues are different in structure.

## Slide 56: Scalar Maps: Fractional Anisotropy
FA(D) is intrinsic to the tissue and is independent of fiber orientation, and diffusion sensitizing gradient directions
FA(D) is useful to characterize the shape (degree of ‘out-of-roundness’) of the diffusion ellipsoid
Low FA: High FA:

## Slide 57: Fractional Anisotropy
Fill in the following information:
-Set Input DTI Volume to ‘dti’
-Select Output Scalar Volume ‘Create new Volume as ...’ and name it ‘fa’
-In ‘Scalar Measurement’, select ‘Fractional Anisotropy’
-Click on Apply to calculate the Fractional Anisotropy map of the tensor volume

## Slide 58: Fractional Anisotropy
The FA image appears in the yellow viewer
Set L as none.

## Slide 59: Fractional Anisotropy
Position your mouse over the pin icon and click the ‘>>’ icon to display this table. Set the background volume to ‘fa’ and be sure the foreground volume is still set to ‘dti’ with opacity at 0.40

## Slide 60: Fractional Anisotropy
Explore the FA values in the Corpus Callosum and in adjacent gray matter areas. Note how the FA values are high in the white matter areas, and low in gray matter regions

## Slide 61: Fractional Anisotropy
Change to Conventional view

## Slide 62: Part 2: Visualizing the tensor data

## Slide 63: 3D Visualization: Glyphs
Click on the Modules menu and select the module Volumes

## Slide 64: 3D Visualization: Glyphs
Position the mouse over the pin icon and select the ‘<<‘ icon to display the axial slice toolbar. Set the Foreground to ‘fa’ and the Background to ‘dti’, with the Foreground opacity set to 1.00

## Slide 65: 3D Visualization: Glyphs
Set the Active Volume to ‘dti’ and the Scalar Mode to ‘ColorOrientation’

## Slide 66: 3D Visualization: Glyphs
Scroll down the module panel and in the Glyphs on Slices Display section:
-Check off the option for Red, Yellow, and Green Slice Visibility
-Set the Color by Scalar parameter to ‘ColorOrientation’
-Set the Glyph Type to ‘Ellipsoids’

## Slide 67: 3D Visualization: Glyphs
The glyphs appear in all 3 slice viewers

## Slide 68: 3D Visualization: Glyphs
Position your mouse over the pin icon select the eye icon to display the axial, coronal, and sagittal slices in the 3D viewer

## Slide 69: 3D Visualization: Glyphs
Slicer displays the anatomical slices in the 3D viewer

## Slide 70: 3D Visualization: Glyphs
Zoom in to observe the glyphs. The ellipsoids represent the principal direction of diffusion (main eigenvector)

## Slide 71: Diffusion MRI tractography
Deselect the option for Red, Yellow, and Green Slice Visibility, and deselect the eye icon

## Slide 72: Diffusion MRI tractography
Position your mouse over the pin icon and change the Foreground to ‘None’ and the background to ‘fa’
Click pin icon and then L to reset the 3D view to left

## Slide 73: Part 3: From tensors to tracts

## Slide 74: DTI tractography
Definition of a region of interest (ROI) for seeding tract in an FA map (Editor module)
Single-tensor tractography (Tractography Interactive Seeding module)
Fiducial-seeding tractography (Tractography Interactive Seeding module)

## Slide 75: Diffusion MRI tractography
Click all modules and select the module Editor

## Slide 76: Diffusion MRI tractography
Set Master Volume to be “fa”
Select Merge volume “Create new LabelMap Volume”
Click on OK in the window popped out

## Slide 77: Diffusion MRI tractography
Select the Yellow slice only layout

## Slide 78: Diffusion MRI tractography
Select the DrawEffect tool

## Slide 79: Diffusion MRI tractography
Outline the contour of the Corpus Callosum with the DrawEffect tool and press enter. Repeat this step with 3 adjacent sagittal slices

## Slide 80: Diffusion MRI tractography
In the next section, we will seed tracts from this anatomical region of interest.

## Slide 81: Diffusion MRI tractography
Click on the Modules and then select Diffusion -> Tractography->Tractography Seeding.

## Slide 82: Step1: I/O
-Set the Input DTI Volume to ‘dti’
-Set Output Fiber Bundle to ‘corpusCallosum’ by renaming the default parameter ‘Fiber Bundle’
-Set the Input Fiducials, Model or Label Map to ‘fa-label’
Change to Conventional view

## Slide 83: Step 2: Seeding parameters
Select the default Tractography Seeding parameters:
- Threshold Type: FractionalAnistropy
- Seeding Threshold:0.30
- Stopping Threshold: 0.25
Click Update to generate tractography

## Slide 84: Step 3: Generate Tracts
The tracts generated in the corpus callosum area appear in the 3D viewer.
The fibers are colored by their mean fiber orientations with red, green and blue representing right-left, anterior-posterior and inferior-superior direction.

## Slide 85: Step 4: Undesirable track removal
Click on the Modules menu, then select Diffusion -> Tractography -> Tractography Display

## Slide 86: Step 4: Undesirable track removal
Click Fiber Bundle Selection

## Slide 87: Step 4: Undesirable track removal
In ‘Fiber Bundle Selection’, under ROI for Fiber Select, create a new AnnotationROI as ‘ROI node’ and select Disable ROI.

## Slide 88: Step 4: Undesirable track removal
Adjust the ROI frame to include the undesirable tracks, using the colorful spheres provided.

## Slide 89: Step 4: Undesirable track removal
Click on Negative ROI to finish

## Slide 90: Step 4: Undesirable track removal
Uncheck ROI Visibility

## Slide 91: Fiducial Seeding
Click on the Modules and then select Diffusion -> Tractography->Tractography Seeding.

## Slide 92: Fiducial Seeding
Position the mouse over the pin icon and click on the eye icon to display the axial slice in the 3D viewer
Unlink the link icon

## Slide 93: Fiducial Seeding
Select the module Markups

## Slide 94: Fiducial Seeding
Click on the arrow icon to create a fiducial

## Slide 95: Fiducial Seeding
Position the fiducial in the left cingulum of the coronal slice

## Slide 96: Fiducial Seeding
Double click on the fiducial and change the name to LeftCingulum

## Slide 97: Fiducial Seeding
Click on the Modules and then select Diffusion -> Tractography->Tractography Seeding.
Set the Input DTI volume to ‘dti’
Set the Input Fiducials, Model or Label Map to ‘F’
Select the Output Fiber Bundle ‘Create New Fiber Bundle as ...’ and name it ‘Cingulum’
Click Update

## Slide 98: Fiducial Seeding
Part of the left cingulum appears in the 3D viewer.
Move the fiducial and update the Left Cingulum fiducial to explore the spatial relationship between the left cingulum and the corpus callosum

## Slide 99: Tractography ‘on-the-fly’
Select the module Markups

## Slide 100: Tractography ‘on-the-fly’
Click on the arrow icon to create a new fiducial, and position it in the 3D viewer
Select the List ‘Create new MarkupsFiducial’

## Slide 101: Tractography ‘on-the-fly’
Click on the Modules and then select Diffusion -> Tractography->Tractography Seeding.
Set the Input DTI volume to ‘dti’
Set the Input Fiducials, Model or Label Map to ‘F_1’
Select the Output Fiber Bundle ‘Create New Fiber Bundle as ...’ and name it ‘TractOnTheFly’
Check Update (check for interactive)

## Slide 102: Tractography ‘on-the-fly’
Move the fiducial F_1-1 in the 3D viewer to explore the dti dataset

## Slide 103: Tractography ‘on-the-fly’
The Fiducial Seeding functionality allows you to do tractography ‘on-the-fly’ to explore white matter structures interactively

## Slide 104: DTI Analysis
Select the module Data to display the list of elements that have been generated in this tutorial

## Slide 105: Conclusion
This tutorial guided you through the different steps of a Diffusion MR analysis pipeline, from tensor estimation to 3D tracts visualization, for exploring and studying the 3D architecture of the brain white matter.

## Slide 106: Acknowledgments
Open Source Diffusion MRI Technology For Brain Cancer Research NIH U01CA199459
National Center for Image Guided Therapy (NCIGT)
NIH P41EB015898
Neuroimage Analysis Center (NAC)
NIH P41EB015902
Tutorial updated by
Fan Zhang, Ph.D. Brigham and Women’s Hospital, Harvard Medical School
Mengying Zhang, undergraduate National University of Singapore