## Slide 1
Exploring Peritumoral White
Matter Fibers for
Neurosurgical Planning
Sonia Pujol, Ph.D.
Ron Kikinis, M.D.
Surgical Planning Laboratory Harvard University

## Slide 2
Clinical Goal
Diffusion Tensor Imaging
(DTI) Tractography has the potential to bring valuable
spatial information on tumor
infiltration and tract
displacement for
neurosurgical planning of
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
tumor resection.

## Slide 3
Clinical Case
•
35 year-old male
diagnosed with
Glioblastoma multiform
(GBM)
• Diffusion Weighted
Imaging (DWI)
acquisition for
neurosurgical planning

## Slide 4
Clinical Goal
White Matter tracts
Tumor
Ventricles
The goal of this tutorial is to explore white matter
fibers surrounding a
tumor using Diffusion Tensor Imaging (DTI) Tractography.

## Slide 5: Slicer DMRI
An open-source project to improve and extend diffusion magnetic resonance imaging software in 3D Slicer:
http://dmri.slicer.org Please read the Diffusion MRI Analysis tutorial to install SlicerDMRI:
http://dmri.slicer.org/docs/diffusion_mri_analysis

## Slide 6
Image Analysis Pipeline
The image analysis pipeline
described in this tutorial uses three different algorithms:
1) Grow Cut algorithm for segmentation of the tumor parts
2) Marching Cube algorithm for surface modeling
3) Single tensor streamline tractography algorithm for tract generation.

## Slide 7
Overview of the analysis pipeline
Part 1: Loading & Visualization of Diffusion Data
Part 2: Segmentation of lat. ventricles, and solid
and cystic parts of the tumor
Part 3: Tractography reconstruction of white
matter fibers in the peri-tumoral volume
Part 4: Tractography exploration of the
ipsilateral and contralateral side

## Slide 8
Part 1: Loading and Visualization of Diffusion Data

## Slide 9
Diffusion Tensor Imaging
(Stejskal and Tanner 1965, Basser 1994 )
D=
D
D
D
xx
yx
zx
D
D
D
xy
yy
zy
D
D
D
xz
yz
zz

## Slide 10: Tutorial Data
Please download sample data at
https://www.slicer.org/slicerWiki/images/b/bb/WhiteMatterExplorationData.zip

## Slide 11
Loading DTI and Baseline Data
Drag and drop both the “BaselineVolume.nrrd and DTIVolume.nhdr files to the Slicer window

## Slide 12
After dragging and dropping the “.nrrd and .nhdr volume files” into the Slicer window, click on OK
Loading DTI and Baseline Data

## Slide 13
Loading DTI and Baseline Data
Slicer has loaded the DTI volume and the baseline image.

## Slide 14
Loading DTI and Baseline Data
Click on the pin icon to display the slice menu, then click on the link
icon
to link the 3
anatomical viewers.
Then change the
background so it is set to BaselineVolume

## Slide 15
Loading DTI and Baseline Data
Select the Volumes module from the Modules menu

## Slide 16
Loading DTI and Baseline Data
The user can manually adjust the Window Level editor presets with the Volume module menu

## Slide 17
Loading DTI and Baseline Data
Click on the Layout menu and select the layout Red Slice only

## Slide 18
Part 1:
Segmenting the
tumor and ventricles

## Slide 19
Tumor Segmentation
The tumor in this clinical case is
composed of two parts: a solid part, and a cystic part.
In this section, we will segment the different parts of the tumor
using a Grow Cut Segmentation
algorithm.

## Slide 20
Tumor Segmentation
White Matter Exploration for Neurosurgical Planning
Sonia Pujol, Ph.D. - Ron Kikinis, M.D.
NA-MIC ARR 2012-2015
Slicer displays only the Axial anatomical slice in the Viewer

## Slide 21
Tumor Segmentation
White Matter Exploration for Neurosurgical Planning
Sonia Pujol, Ph.D. - Ron Kikinis, M.D.
NA-MIC ARR 2012-2015
Go to All modules and click on the Modules menu and select the module Editor

## Slide 22
Tumor Segmentation
White Matter Exploration for Neurosurgical Planning
Sonia Pujol, Ph.D. - Ron Kikinis, M.D.
NA-MIC ARR 2012-2015
The ‘SlicerApp-real’ window appears. Select the label map GenericAnatomyColors and click OK.

## Slide 23
Tumor Segmentation
White Matter Exploration for Neurosurgical Planning
Sonia Pujol, Ph.D. - Ron Kikinis, M.D.
NA-MIC ARR 2012-2015
Select the PaintEffect

## Slide 24
Tumor Segmentation
White Matter Exploration for Neurosurgical Planning
Sonia Pujol, Ph.D. - Ron Kikinis, M.D.
NA-MIC ARR 2012-2015
Scroll down the Editor module.
Click the color bar to search the pre-defined label.

## Slide 25
Tumor Segmentation
White Matter Exploration for Neurosurgical Planning
Sonia Pujol, Ph.D. - Ron Kikinis, M.D.
NA-MIC ARR 2012-2015
Input cyst and select number 309 for cystic part of the tumor.

## Slide 26
Tumor Segmentation
White Matter Exploration for Neurosurgical Planning
Sonia Pujol, Ph.D. - Ron Kikinis, M.D.
NA-MIC ARR 2012-2015
Set Radius to 4

## Slide 27
Tumor Segmentation
White Matter Exploration for Neurosurgical Planning
Sonia Pujol, Ph.D. - Ron Kikinis, M.D.
NA-MIC ARR 2012-2015
In a single motion, draw a a circle in the cystic part of the tumor in 3 continuous frames.

## Slide 28
Tumor Segmentation
White Matter Exploration for Neurosurgical Planning
Sonia Pujol, Ph.D. - Ron Kikinis, M.D.
NA-MIC ARR 2012-2015
Input mass and select number 7 for solid part of the tumor.

## Slide 29
Tumor Segmentation
White Matter Exploration for Neurosurgical Planning
Sonia Pujol, Ph.D. - Ron Kikinis, M.D.
NA-MIC ARR 2012-2015
In a single motion, draw a a line in the solid part of the tumor in 3 continuous frames.

## Slide 30
Tumor Segmentation
White Matter Exploration for Neurosurgical Planning
Sonia Pujol, Ph.D. - Ron Kikinis, M.D.
NA-MIC ARR 2012-2015
Select color #107 and draw a circle around the solid and cystic parts of the tumor.

## Slide 31
Tumor Segmentation
White Matter Exploration for Neurosurgical Planning
Sonia Pujol, Ph.D. - Ron Kikinis, M.D.
NA-MIC ARR 2012-2015
Select the GrowCutEffect tool.

## Slide 32
Grow Cut Segmentation
• The Grow Cut Segmentation method is a competitive region growing algorithm using Cellular Automata.
• The algorithm performs multi-label
image segmentation using a set of user input scribbles.
• V. Vezhnevets, V. Konouchine. "Grow-
Cut" - Interactive Multi-Label N-D Image Segmentation". Proc. Graphicon. 2005 . pp. 150-156.

## Slide 33
Tumor Segmentation
White Matter Exploration for Neurosurgical Planning
Sonia Pujol, Ph.D. - Ron Kikinis, M.D.
NA-MIC ARR 2012-2015
Click Apply to apply the GrowCutEffect segmentation algorithm.

## Slide 34
Tumor Segmentation
White Matter Exploration for Neurosurgical Planning
Sonia Pujol, Ph.D. - Ron Kikinis, M.D.
NA-MIC ARR 2012-2015
Slicer displays the results from the segmentation
Cystic part
Solid part

## Slide 35
Tumor Segmentation
Scroll up the Editor menu and select the tab Per-Structure Volumes. Then click Split Merge Volume.

## Slide 36
Tumor Segmentation
Click on the Modules menu and select the Module Data.

## Slide 37
Tumor Segmentation
The different label maps have been generated.

## Slide 38
Ventricles Segmentation
Go back to the Editor module.

## Slide 39
Ventricles Segmentation
Select the volume BaselineVolume-ventricles of brain-label.
A

## Slide 40
Ventricles Segmentation
Select the ThresholdEffect tool.
.

## Slide 41
Ventricles Segmentation
Scroll down the Editor module, set the lower Threshold Range to 1700 and click Apply
.

## Slide 42
Ventricles Segmentation
Slicer displays the result of the threshold
.

## Slide 43
Ventricles Segmentation
Select the SaveIslandEffect in the Editor module.
.

## Slide 44
Ventricles Segmentation
Click in the occipital horn of the ventricle .

## Slide 45
Slicer displays the results of the segmentation of the lateral ventricle.
Ventricles Segmentation

## Slide 46
Scroll back up and cllick on Merge and Build to merge the three label maps, and generate 3D models of the tumor and ventricles using a Marching Cubes algorithm.
Ventricles Segmentation

## Slide 47
Final Result of Segmentation
Slicer displays the results of the merging of the three labelmaps in the 2D viewer.

## Slide 48
Final Result of Segmentation
Click on the Layout menu and select Conventional.

## Slide 49
Final Result of Segmentation
Slicer displays the 3D surface reconstructions of the ventricles, and solid and cystic parts of the tumor.

## Slide 50
Definition of peri-tumoral volume
Position the mouse over the pin icon, deselect the link icon, and select the eye icon to view just the axial slice in the 3D viewer.

## Slide 51
Definition of peri-tumoral volume
Select the label map BaselineVolume-cyst-label (yellow) and select the DilateEffect tool.

## Slide 52
Definition of peri-tumoral volume
With the DilateEffect tool equipped, click on the cystic part of the tumor in the axial slice viewer once, then select Apply 3 times to generate the peritumoral volume
Note the dilation of the cystic part of the tumor in the 3D Viewer.

## Slide 53
Part 2: Tractography
exploration of peri-
tumoral white matter
fibers

## Slide 54
Tractography LabelMap Seeding
Click on the Modules menu, then select Diffusion ->
Tractography -> Region-based -> Tractography ROI Seeding

## Slide 55
Go to I/O and set the following values:
Input DTI Volume: DTIVolume
Input Label Map: BaselineVolume-cyst-label
Output Fiber Bundle: Create and rename newFiberBundle
Tractography LabelMap Seeding

## Slide 56
Scroll down and set the following values:
Check Use Index Space
Tractography LabelMap Seeding

## Slide 57
Tractography LabelMap Seeding
Scroll down to Tractography Seeding Parameters and set the following values:
Set Stopping Criteria to FractionalAnisotropy
Set Stopping Value to 0.15
Scroll down to Label Definition and set the following values:
Set Seeding Label to 309 (cyst)
Click on Apply

## Slide 58
Slicer displays the white matter fibers surrounding the tumor
The fibers are colored according fractional anisotropy values (red = low FA; blue,green=high FA)
Tractography LabelMap Seeding

## Slide 59
Part 4: Tractography
exploration of the
ipsilateral and
contralateral side

## Slide 60
Tractography on-the-fly
Click on the Modules menu, then select Diffusion ->
Tractography -> Tractography Seeding
NA-MIC ARR 2012-2015

## Slide 61
Tractography on-the-fly
Position the mouse over the pin icon in the axial slice viewer and change the volume to DTIVolume

## Slide 62
Tractography on-the-fly
Select the Fiducial icon, and position it next to the cystic part
of the tumor by clicking near it in the 3D viewer

## Slide 63
Tractography on-the-fly
Set Input DTI Volume to DTIVolume Set Fiducial List or Model to F
Set Output Fiber Bundle to Create new Fiber Bundle

## Slide 64
Tractography on-the-fly
Scroll down the module and set
the Minimum Path Length to
10.0 mm and the FA Stopping Value at 0.15

## Slide 65
Tractography on-the-fly
Position the fiducial in the cingulum on the contralateral side opposite to the tumor

## Slide 66
Tractography on-the-fly
Explore the aspect of the cingulum in the contralateral and ipsilateral sides

## Slide 67
Conclusion
• Fully integrated pipeline for semi-
automated tumor segmentation and white matter tract reconstruction
• 3D interactive exploration of the white
matter tracts surrounding a tumor (peri-
tumoral tracts) for neurosurgical planning

## Slide 68
Acknowledgments
National Alliance for Medical Image
Computing (NA-MIC)
NIH U54EB005149
•
•
Neuroimage Analysis
NIH P41RR013218
Center
(NAC)
Parth Amin, WIT, Farukh Kohistani, BC,
Fan Zhang, University of Sydney
Shun Gong, Shanghai Changzheng Hospital
Mengying Zhang, National University of Singapore
•